## Slide 1: IP presentation
Nolan Luckett
05/02/18

## Slide 2: Introduction
Zynq PS’s I2C Interface
Xylon’s I2S IP

## Slide 3: I2C Interface
The Zynq PS provides an I2C interface that can be used to communicate with external hardware.

## Slide 4: I2C Configuration
Enable the I2C Interface in the Zynq Configuration window

## Slide 5: I2C Connections
Connect the I2C output to the audio codec’s serial data and clock lines

## Slide 6: I2C Software
Configure the I2C component:
  XIicPs_LookupConfig
  XIicPs_CfgInitialize
  XIicPs_SetSClk
Send address/data
  XIicPs_MasterSendPolled
Example Level 1 driver available from the Zynq book

## Slide 7: Audio codec configuration
void AudioPllConfig(XIicPs *Iic) {
AudioWriteToReg(Iic, R15_SOFTWARE_RESET, 0b000000000); //Perform Reset
usleep(75000);
AudioWriteToReg(Iic, R6_POWER_MANAGEMENT, 0b000110000); //Power Up
AudioWriteToReg(Iic, R0_LEFT_CHANNEL_ADC_INPUT_VOLUME, 0b000010111); //Default Volume
AudioWriteToReg(Iic, R1_RIGHT_CHANNEL_ADC_INPUT_VOLUME, 0b000010111); //Default Volume
AudioWriteToReg(Iic, R2_LEFT_CHANNEL_DAC_VOLUME, 0b001100000);
AudioWriteToReg(Iic, R3_RIGHT_CHANNEL_DAC_VOLUME, 0b001100000);
AudioWriteToReg(Iic, R4_ANALOG_AUDIO_PATH, 0b000010010); //Allow Mixed DAC, Mute MIC
AudioWriteToReg(Iic, R5_DIGITAL_AUDIO_PATH, 0b000000111); //48 kHz Sampling Rate emphasis, no high pass
AudioWriteToReg(Iic, R7_DIGITAL_AUDIO_I_F, 0b001000010); //Master, I2S Mode, 16 bits
AudioWriteToReg(Iic, R8_SAMPLING_RATE, 0b000000000);
usleep(75000);
AudioWriteToReg(Iic, R9_ACTIVE, 0b000000001); //Activate digital core
AudioWriteToReg(Iic, R6_POWER_MANAGEMENT, 0b000100010); //Output Power Up
}

## Slide 8: I2S IP
This IP is provided by Xylon with an evaluation license. It provides an AXI interface for interacting with audio codecs with an I2S interface.

## Slide 9: I2S IP Configuration
Configure 2 Instances
  1x Transmitter
  1x Receiver
Configure both to be clock slaves

## Slide 10: I2S IP Connections
Connect the bit and word select clock outputs from the audio codec to the IP.
Connect the Audio inputs and outputs to the IP
Connect the interrupt output to the IRQ_F2P input on the PS, concatenating as necessary

## Slide 11: I2s ip driver
A Linux driver was provided, modified for the standalone OS by substituting Linux headers with Xilinx headers. (primarily related to IO)
Level 1 driver providing simplified register interactions for common tasks, e.g:
  u32 logii2s_port_read_fifo_word(struct logii2s_port *port);
  void logii2s_port_write_fifo_word(struct logii2s_port *port, u32 data);
  void logii2s_port_clear_isr(struct logii2s_port *port, u32 bit_mask);
  void logii2s_port_enable_xfer(struct logii2s_port *port);
  void logii2s_port_disable_xfer(struct logii2s_port *port);

## Slide 12: Recording flowgraph
Create Handler for I2S Interrupt:
Configure the GIC
Connect the handler to the event
Enable Recording:
Clear ISR
Unmask Interrupts
Enable Transfer
Process the FIFO Almost Full Event:
Copy the data from the FIFO into memory
Clear ISR
Interrupt

## Slide 13: References
Section 5C of “The Zynq Book Tutorials”
Digilent Zybo Reference